## Slide 1: Night Driving
Masters N-A through N-Q

## Slide 2: Night Driving Objectives
1. Problems associated with night driving
2. Special pre-driving procedures for night driving
3. Visual searching techniques for night driving
4. Reducing glare associated with night driving
5. Reducing the risk of overdriving your headlights
6. Reducing the risk of certain maneuvers at night

## Slide 3: Night Time Death Date vs Day Time Death Rate
Rural Areas 2 ½ Times Greater
Urban Areas 3 Times Greater

## Slide 4: Sight Distance At Night
Low Beams High Beams
Stationary Vehicle 150 feet 500 feet
Vehicle at 30 mph 90 feet 300 feet

## Slide 5: Low Reflective Objects
Any person, vehicle or animal that is adjacent to the roadway with little to no reflection is difficult to see beyond 70 feet.

## Slide 6: Slower Reaction Time
At night, you can add anywhere from 1.5 to 2.0 seconds reaction distance to your normal reaction distance.
Reaction Distance = Speed x 1.47 x Reaction Time x Night Reaction Time
Normal Reaction Time Night Reaction Time, 1.5
.75 at 35 mph (Day) = 39 feet, at night = 58 feet
.75 at 55 mph (Day) = 61 feet, at night = 91 feet
1.0 at 35 mph (Day) = 52 feet, at night = 77 feet
1.0 at 55 mph (Day) = 81 feet, at night = 121 feet

## Slide 7: Headlight Glare
  Approaching vehicle on low beam, maximum visibility is 200 feet
  When approaching vehicle is on low beam at 100 feet distance, the ability to see objectives adjacent to roadway is reduced
  Can be momentarily blinded for as long as 7 seconds
  Vehicles behind and alongside

## Slide 8: Depth Perception
Estimating closing speed of oncoming vehicles and following distance
Estimating closing speed of ongoing vehicles

## Slide 9: Search Patterns
Need to fixate longer on objects
Need to check edge of road

## Slide 10: Special Pre-Ignition and Ignition Procedures
1. Check Intended Path of Vehicle
2. Clean Windows and Lights
3. High/Low Beam
4. Panel Lights
5. Rearview Mirror
6. Side View Mirrors
7. Periodic Check of All Lights

## Slide 11: Special Search Techniques
Search to the limits of your headlights range
Periodically search beyond the range of headlights
Use the right lane edge line or fog line to help in positioning your vehicle

## Slide 12: Reducing Headlight Glare
Use right lane line with approaching vehicle
Adjust mirrors

## Slide 13: Reducing Risk of Overdriving Headlights
Increase your following distance
Use headlights of ongoing vehicles
Visual clues outside of lateral range of headlights

## Slide 14: Turns and Curves
Reduce Speed
Search beyond the lateral range of the headlights
Don’t allow eyes to only follow headlight range

## Slide 15: Backing
Check intended path
Slow speed and look in direction

## Slide 16: Changing Lanes
Practice judging closing speed of vehicles from behind
Allow extra clearance

## Slide 17: Risks of Passing at Night
Limited range of headlights
Overdriving headlights
Other drivers inability to determine speed of closing
*Reasons for passing at night seldom justify the risks

## Slide 18: Stopping Along Shoulder of Highway
Unless it is an emergency, Don’t
As far off roadway as shoulders allow
Four-Way Flashers
Flairs or Reflectors
Safest Area for Passengers

## Slide 19: Contact/Mission
For more information on the (the topic of the presentation) please visit PDE’s website at www.education.pa.gov
The mission of the Department of Education is to ensure that every learner has access to a world-class education system that academically prepares children and adults to succeed as productive citizens. Further, the Department seeks to establish a culture that is committed to improving opportunities throughout the commonwealth by ensuring that technical support, resources, and optimal learning environments are available for all students, whether children or adults.